## Slide 1
Microcontrollers
Arduino
SUTD ORGANIZATION OF AUTONOMOUS ROBOTICS
Notes: I will be talking about microcontrollers today and you will be using this for your soar challenge. Arduino will be used to teach in this course.

## Slide 2: Arduino IDE
https://www.arduino.cc/en/software
A compiler to program an Arduino microcontroller.
Do not install from “Windows app”.
5 Minutes
Notes: Before we start, I will need all of you to enter the following link and download the latest Arduino compiler for this course. Do not install the windows app.

## Slide 3: Microcontrollers
An integrated circuit board.
Many inputs/outputs pins.
Programmable to perform certain task.
Not all microcontrollers are built the same
Introduction
Notes: So, what is a microcontroller? A microcontroller is an integrated circuit board, with many inputs and output pins, and can be programmed to perform task. However, not all microcontroller are built the same.

## Slide 4: How to choose a microcontroller?
Cost
System requirements
Notes: Since not all microcontroller are build the same, then how do I choose it? It depends on the cost and the system requirements of your project.
For instance, you need faster clock speed, better audio output, smaller controller, more memory, etc.
Of course you may get the best microcontroller for all of your projects but that will incur a higher cost for your project. Its like buying an intel i9 CPU to run only on word document.

## Slide 5: Microcontrollers
PIC
Arduino
Teensy
Rasberry Pi
Notes: When I say microcontroller, I do not mean I know how to program an Arduino, but knowing the basic fundamental of a microcontroller and program them to perform specific task. This slides shows some brands or company that manufacture microcontroller. All these microcontrollers require different compiler but the methods used in programming are the same.

## Slide 6
Check the voltage requirement of the microcontroller!
(Fireworks may occur)
Notes: Always check the input/output voltage of the microcontroller. Different devices run on different voltage, the most common ones are 3.3V, 5V and 9V. You rarely see 36V but they do exist.

## Slide 8: Arduino

## Slide 9
Microcontrollers are still too EXPENSIVE!
Notes: Always check the input/output voltage of the microcontroller. Different devices run on different voltage, the most common ones are 3.3V, 5V and 9V. You rarely see 36V but they do exist.

## Slide 10: 3rd Party Microcontroller
Do not differ much from the original unless your program is computing intensive.
Some uses a different chipset.
Some require additional driver.

## Slide 11: CH340 Driver
https://sparks.gogo.co.nz/ch340.html
- Driver to run the Chinese make 3rd party Arduino
5 Minutes
Notes: Before we start, I will need all of you to enter the following link and download the latest Arduino compiler for this course. Do not install the windows app.

## Slide 12: Built in functions in a microcontroller
5V
Ground
PWM
Digital input/Output
Analog input/Output
Timer
Interrupts
Communications
Read notes if you are interested!

## Slide 13: Arduino Compiler
Verify
Upload
Board type
Baud rate
Com port
Install new libraries
Getting examples code

## Slide 14
Arduino file is called “Sketch”
setup() runs once on boot up
loop() runs constantly after running setup()
Verify sketch
Compile and flash sketch to arduino
Serial Monitor
Notes: Teach Serial monitor before moving on to blink led

## Slide 15: Rules to programming
Import/ Include
Declare pins
Declare and initialize
Setup
Program

## Slide 16: Variables
Global
  Variable used by many function
Local
  Variable used within a function.
Global Variable
Local Variable
Function

## Slide 17: Other Microcontroller
#define
  To define a pin instead of using “int”
Different pin naming
Declare a function in order to use the function
PIC controller

## Slide 18: Serial Communication
Task:
  Set Baudrate
  Print “Hello World”
  Read from comport
User’s Input
Serial prints
Change Baudrate

## Slide 19: Programming microcontroller
Import
Functions
Loops
Conditionals
Operators
Next Lesson!

## Slide 20: Schematics
A blueprint for a component.
Shows how the component is wired.

## Slide 21: Basic symbols
Ground
Power Source
Battery
Power
Diode
LED
Crystal
Transistor
Resistors
Variable Resistors
Light Dependent Resistor
Transformer
Light bulb
Switch
Switch
Push buttons
Electrolyte Capacitor
Ceramic Capacitor
Required to understand how circuit work!
How individual component work?
ATTEND PHYSICS LESSON!

## Slide 22: Hints on some circuit
Smoothen signals
Ensure circuit runs at a constant voltage
Allows the running of components that require more power than what the microcontroller can provide
Higher resistance equals lower power consumption.
Can be used to read high voltage signal with lower power consumption.
Capacitor
Transistors
Resistors

## Slide 23: Activity (Blinking LED)
Open blinking LED examples
Run blinking
Print the state of the LED

## Slide 24: How does it work?
Look at pin 13 wiring
LED_BUILTIN is not editable
LED_BUILTIN references to pin 13 (on board LED)